## Slide 1: North Topsail Beach ARPA Application Summary
April 5, 2023

## Slide 2: Background
Phase 1 and 2 of the Resilient Coastal Communities Program developed a project list for each Town.
3 Towns and the Community Action Team (CAT) unanimously approved these project sites for evaluation and implementation.
The presented solutions utilize nature-based designs, implement as little gray infrastructure as possible and are designed to infiltrate as much runoff as possible.

## Slide 3: NCRCCP Phase 3 Grant
NCRCCP Objectives
Natural/Nature-Based and Hybrid Solutions
Hazard Mitigation
Environmental Quality
Economic Prosperity
Key Project Benefits
Provide additional storage off the road
Encourage infiltration to mitigate flooding

## Slide 4: Project Overview
Municipalities
Town of North Topsail Beach,
Town of Surf City
Town of Topsail Beach
18 Hot Spot Sites
10 in North Topsail Beach
5 in Surf City
3 in Topsail Beach
North Carolina Resilient Coastal Communities Program (NCCRP) Phase 3
Consistent Standards
Prepare for Permitting and Implementation
Insert Map showing all 18 Hotspots
NCRCCP Phase 3 Sites – 18 Hotspots

## Slide 5: North Topsail Beach

## Slide 6: Type of Infiltration Infrastructure

## Slide 7: Infiltration Swale
Bioswale

## Slide 8: Infiltration Chamber

## Slide 9: How it works
Infiltration System with pumps
Seasonally high-water table

## Slide 10: Dune Infiltration

## Slide 11: Permeable Pavers
Permeable Pavers - Sidewalk and Street Style
Permeable Pavers – Standard parking Style

## Slide 12: ARPA LASII Funding

## Slide 13: Local Assistance for Stormwater Infrastructure Investments Program (LASII)
Key Considerations
Documentation of Stormwater Quantity or Quality Issues.
Demonstration of “Significant Hardship Raising the Revenue”.
Council Resolution
Funding Opportunities (Spring 2023)
$6.3 Million allocated for Stormwater Planning Applications
No Matching Funds are Required
Application Due by May 1st, 2023.

## Slide 14
-23.10 %
$54,167

## Slide 15: Hotspot solutions

## Slide 16: Town of North Topsail Hotspots

## Slide 17: Hotspot 4
Hotspot 5

## Slide 18: Hotspot 4- Infiltration Chambers
Hotspot 5- Infiltration Swales

## Slide 19: Hotspot 6
Hotspot 7

## Slide 20: Hotspot 6- Infiltration Swale
Hotspot 7- Infiltration Chamber

## Slide 21: Hotspot 8
Hotspot 9

## Slide 22: Hotspot 8
Hotspot 9- Bioswale
Infiltration Swale
Pavers & Level Spreader

## Slide 23: Hotspot 10
Hotspot 11

## Slide 24: Hotspot 10 – Infiltration Swale
Hotspot 11- Permeable Pavers

## Slide 25: Hotspot 12
Hotspot 13

## Slide 26: Hotspot 12 – Bioswale
Hotspot 13- Rip Rap Swale

## Slide 27: Hotspot 4

## Slide 29
Estimated Construction Costs

## Slide 30
Infiltration Swale
Pavers & Level Spreader

## Slide 32
Estimated Construction Costs

## Slide 33
LASII Funding Request Recommendation

## Slide 34: Questions?
Marc Horstman, PE, PH, D.WRE
Senior Project Manager
mhorstman@wkdickson.com
www.wkdickson.com

## Slide 35: Investigation & Analysis

## Slide 36: Project Approach
Key Considerations
Minimize Property Impact
  ROW
  Easements
  Municipal Properties
Water Off the Road
Water Table
Soil Porosity
Municipality
Additional Considerations
NCDOT Standards
NCDEQ MDC’s
Bioswale, Infiltration Swale, Infiltration Chamber, Dune Infiltration & Permeable Pavers

## Slide 37: Infiltration Infrastructure
How It Works
  Captures runoff from roadway
  Provides additional storage
  Infiltrates water into the sandy soils
    Provides path for surface water to leave
    Improves runoff Water Quality
Optional

## Slide 38: Investigation
Visited all 18 hotspots
Identified feasible solutions and surface potential challenges
Infiltration Testing
Seasonal High Water Table (SHWT)
Ground Water Table (GWT)
Survey
LiDar
Field Investigation
Infiltration and Ground Water Testing
Survey and LiDar

## Slide 39: Key Observations From Investigation
Limited available ROW, easement & Real Estate
Utilities occupy existing ROW
Limited active existing drainage infrastructure
SHWT and GWT depths vary significantly
Ground Water Table (GWT)
Elevation and available cover is minimum
Some sites will require wetland consideration
Field & Desktop Investigation
Infiltration and Ground Water Testing
Survey and LiDar

## Slide 40: How it works
Dune Infiltration System with pumps
SHWT
Groundwater Table (GWT)

## Slide 41
Hotspot Seasonal High Water Table (SHWT) and Groundwater Table (GWT) Depths |  |  |  | 
Hotspot # | Municipality | Site | SHWT Depth Ground to SWHT (Inches) | GWT Depth Ground to GWT (Inches)
Site 1a | Topsail Beach | N. Anderson & Sidbury Ave (Infiltration Chambers) | 130 | 143
Site 1b | Topsail Beach | N. Anderson & Sidbury Ave (Dune Infiltration) | 50 | 57
Site 2 | Topsail Beach | S. Anderson Blvd & Barwick Ave | 29 | 36
Site 3 | Topsail Beach | S. Anderson Blvd & Florida Ave | 33 | 45
Site 4 | N. Topsail Beach | Island Drive & Gray Street | 12 | 18
Site 5 | N. Topsail Beach | Island Drive Between 17th Ave & 18th Ave | 7 | 11
Site 6 | N. Topsail Beach | Island Drive Between 2nd Ave & 4th Ave | 50 | 63
Site 7 | N. Topsail Beach | New River Inlet Road Beach Access | 11 | 21
Site 8 | N. Topsail Beach | North Topsail Beach Town Park | 25 | 38
Site 9 | N. Topsail Beach | New River Inlet Road by Seaview Motel | 15 | 21
Site 10 | N. Topsail Beach | Near 1070 New River Inlet Rd | 15 | 23
Site 11 | N. Topsail Beach | New River Inlet Road & Jenkins Way | 27 | 36
Site 12 | N. Topsail Beach | New River Inlet Road & Bay View Drive | 5 | 12
Site 13 | N. Topsail Beach | New River Inlet Road & River Drive | 48 | 56
Site 14 | Surf City | S. Shore Road & Sea Horse Ave | 125 | 134
Site 15 | Surf City | S. Shore Road & Charlotte Ave | 168 | 173
Site 16 | Surf City | S. Shore Road & Roland Ave | 57 | 65
Site 17 | Surf City | N. New River Drive & Mecklenburg Ave | 18 | 24
Site 18 | Surf City | N. New River Drive & Pender Ave | 28 | 34
 |  | Minimum | 5 | 11
 |  | Average | 45 | 53
 |  | Maximum | 168 | 173

## Slide 42: Infiltration Infrastructure Expected Performance
Above 1-2 ft of SHWT
  Consistent infiltration entire year
Above 0-1 ft of SHWT
  Peak infiltration in Spring & Summer
  Reduced infiltration in Fall & Winter
Below 0-0.5 ft of SHWT
  Some infiltration during Spring & Summer
  Min. infiltration during Fall & Winter
Below 0.5-2.0 ft of SHWT
  Primarily acts as storage
  Some infiltration Spring & Summer
  Very little infiltration during Fall & Spring

## Slide 43: Hotspot & SHWT Summary
HotSpots with Infiltration Structure 1-2 ft above SHWT |  | 
Hotspot # | Municipality | Description
Site 1b | Town of Topsail Beach | S. Anderson & Sidbury Ave (Dune Infiltration)
Site 15 | Town of Surf City | S. Shore Road & Charlotte Ave
Site 16 | Town of Surf City | S. Shore Road & Roland Ave
Site 17 | Town of Surf City | N. New River Drive & Mecklenburg Ave
Site 4 | Town of North Topsail beach | Island Drive & Gray Street
Site 13 | Town of North Topsail beach | New River Inlet Road & River Drive
Hotspots with Infiltration Structure 0-1 ft SHWT |  | 
Hotspot # | Municipality | Description
Site 18 | Town of Surf City | N. New River Drive & Pender Ave
Site 7 | Town of North Topsail beach | New River Inlet Road Beach Access
Site 9 | Town of North Topsail beach | New River Inlet Road by Seaview Motel
Site 10 | Town of North Topsail beach | Near 1070 New River Inlet Rd
Site 12 | Town of North Topsail beach | New River Inlet Road & Bay View Drive
Site 14 | Town of North Topsail beach | S. Shore Road & Sea Horse Ave
Hotspots with Infiltration Structure 0-0.5 ft below SHWT |  | 
Hotspot # | Municipality | Description
Site 2 | Town of Topsail beach | S. Anderson Blvd & Barwick Ave
Site 5 | Town of North Topsail beach | Island Drive Between 17th Ave & 18th Ave
Hotspot with Infiltration Structure 0.5-2 ft below SHWT |  | 
Hotspot # | Municipality | Description
Site 1a | Town of Topsail beach | S. Anderson & Sidbury Ave (Infiltration Chambers)
Site 3 | Town of Topsail beach | S. Anderson Blvd & Florida Ave
Site 6 | Town of North Topsail beach | Island Drive Between 2nd Ave & 4th Ave
Site 8 | Town of North Topsail beach | North Topsail Beach Town Park
Site 11 | Town of North Topsail beach | New River Inlet Road & Jenkins Way